## Slide 1: Warm-Up Methodology for HW/SW Co-Designed Processors
A. Brankovic, K. Stavrou, E. Gibert, A. Gonzalez

## Slide 2: Scope
HW/SW co-designed processors (Transmeta-like processors)
  Staged Compilation
    Interpretation, Basic Block Translation, Super-Block Optimization
Transparent Optimization
Layer
CODE CACHE
I$
HW
Guest ISA
(CISC - x86)
Host ISA
(RISC)
TOL

## Slide 3: Scope
Q: How to warm-up the µA state of a HW/SW co-designed processors?
Requirements
LOW ERROR
LOW SIMULATION COST
(3) GENERALY APPLICABLE (tolerant to different TOL and HW setups)
WARM-UP
collect
Warm-Up TOL state + Warm-Up HW state
AUTHORITATIVE EXECUTION
collect
Correct TOL state + Correct HW state
Restore
Architectural Point
L2$ miss ~ 100 cycles
Translation & Optimization
Overhead
TOL
L2$ miss
TOL
~ 10K cycles
TOL overhead creates
2-3 orders of magnitude bigger simulation error
time

## Slide 4: Scope
Contributions
  We solved the problem of the warm-up in HW/SW co-designed processors
  Our solution is based on Downscaling Promotion Thresholds (TH)
    Simulation Error: 0.75%, Simulation Cost Reduction: 65X
Agenda
  Proposed Solution: Downscaling Promotion Thresholds
  Simulation methodology
  Experimental Results
  Conclusions

## Slide 5: Existing solutions
Authoritative simulation
collect
Beginning of application
HW warm-up (wu)
TOL authoritative
collect
HW wu
TOL wu
collect
(AS) Authoritative Simulation
- very costly
(FASS) Fast Authoritative Simulation - costly
NAÏVE – bad error/cost trade-off
Short warm-up -> 100% error
HW wu
TOL wu
collect
(CP) Compilation Plan
- Not generally applicable Depends on Transparent Optimization Layer -TOL
Correct TOL state (Transparent Optimization Layer) + Correct HW state
X
X
X
X
Warm-Up HW state
Warm-Up TOL state
Restore x86 State
Restore x86 State + profiling info & compilation plan
time
More details in the paper

## Slide 6: Downscaling Promotion Thresholds (TH)
During the warm-up, the promotion thresholds are downscaled
  in order to promote faster the code regions to the right compilation stage
HW wu
TOL wu
collect
Restore x86 State
Low Error
Low Simulation Cost
Generally Applicable
Original Threshold
Warm-Up Length (LWU)

time
collect
collect
lower threshold(THWU1)
L1
L2
L3
THWU2
(THWU2> THWU1)
LWU1
LWU2
(LWU2 > LWU1)
>Threshold1
>Threshold2
Interpretation
SB optimization
BB translation
Which pair is better ?
(THWU1 ,LWU1) or (THWU2 ,LWU2)

## Slide 7: Outline
Contributions
  We solved the problem of the warm-up in HW/SW co-designed processors
  Our solution is based on Downscaling Promotion Thresholds (TH)
    Simulation Error: 0.75%, Simulation Cost Reduction: 65X
Agenda
  Proposed Solution: Downscaling Promotion Thresholds
  Simulation methodology
  Experimental Results
  Conclusions

## Slide 8: Simulation Methodology
DARCO infrastructure1
  Transparent Optimization Level - TOL (x86 -> PowerPC)
    Compilation stages: Interpretation, BB translation, SB optimization
    Threshold INT->BB=5, Threshold BB->SB=10K
  Hardware (PowerPC-like)
    2-way issue, in-order, 3 levels memory hierarchy
Suites: SPECint2006 and SPECfp2006
Simulate first 5B x86 instructions
  5 samples per application (at 1B, 2B, 3B, 4B, 5B x86 instructions)
HW
collect
TOL
10M
1M
[1M,10M, 100M, 500M,1B]
1 DARCO: Infrastructure for Research on HW/SW co-designed Virtual Machines. In AMAS-BT'11,, San Jose, June 4, 2011.

## Slide 9: Warm-Up Error Definition
gCPI (guest CPI) error is not enough to be measured
Other statistics are important: Number of host instructions, SuperBlock coverage, etc.
  In order to guide the researchers
error = max(gCPI error, SuperBlock coverage error, #host instruction error)
There are examples where: gCPI error - accurate
SB coverage – inaccurate
#host instructions – inaccurate

## Slide 10: Outline
Contributions
  We solved the problem of the warm-up in HW/SW co-designed processors
  Our solution is based on Downscaling Promotion Thresholds (TH)
    Simulation Error: 0.75%, Simulation Cost Reduction: 65X
Agenda
  Proposed Solution: Downscaling Promotion Thresholds
  Simulation methodology
  Experimental Results
  Conclusions

## Slide 11: Downscaling Promotion Thresholds (TH) - ORACLE
Exploring 50 configurations (10 thresholds x 5 warm-up lengths)
  THWU: [10, 20, 50, 100, 200, 500,1000, 2000, 5000,10K]
  LWU: [1M,10M, 100M, 500M,1B]
TH ORACLE chooses off-line the best pair
LOW ERROR, LOW SIMULATION COST
TH - ORACLE avg 0.4%
Max 4.8%
Cost Red.: 90X
IDEAL SCENARIO
(0% error)
(∞ cost reduction)
Relative error wrt authoritative simulation [%]
Cost reduction wrt authoritative simulation [X]
collect
Original Threshold
Warm-Up Length (LWU)
collect
collect
Lower Threshold
(THWU1)
LWU1
THWU

## Slide 12: Downscaling Promotion Thresholds (TH) - Prediction Model
Predict warm-up threshold and warm-up length based on high-level statistics
Scaled warmed-up execution - similar behavior like authoritative execution
  Based on execution distribution of PCs
Algorithm:
  record execution distribution exec(PCx) during WU1 - for each PC in collect
  find scaling factor - scales the best warm-up to authoritative distribution
    scaling factor = THDEF/THWU
  find the best warm-up period (WU1 or WU2) - scaling error is minimal
    WU1 is better than WU2
collect
exec(PCx)=N1
exec(PCx)=N2
exec(PCx)=N
0
WU2
WU1
AUTHORITHATIVE
PCs
Exec. Counter
PCx
N
N1
N2
AUTH.
WU1
WU2
TH

## Slide 13: Downscaling Promotion Thresholds (TH) – MODEL vs. ORACLE
Exploring 50 configurations (10 thresholds x 5 warm-up lengths)
  THWU: [10, 20, 50, 100, 200, 500,1000, 2000, 5000,10K]
  LWU: [1M,10M, 100M, 500M,1B]
TH ORACLE chose off-line the best pair
TH MODEL when the algorithm is applied
TH MODEL similar to TH ORACLE
TH - MODEL avg 0.75%
Max 16%
Cost Red.: 65X
IDEAL SCENARIO
(0% error)
(∞ cost reduction)
Relative error wrt authoritative simulation [%]
Cost reduction wrt authoritative simulation [X]

## Slide 14: Downscaling Promotion Thresholds (TH) - Different Configurations
Different Transparent Optimization Layers (TOL) configurations:
  without Optimizations
  without Linking
Similar for different HW parameters:
  L1D$: 2X smaller, 2X bigger
  L2U$: 2X smaller, 2X bigger
Model behaves similar for other TOLs

## Slide 15: Outline
Contributions
  We solved the problem of the warm-up in HW/SW co-designed processors
  Our solution is based on Downscaling Promotion Thresholds (TH)
    Simulation Error: 0.75%, Simulation Cost Reduction: 65X
Agenda
  Proposed Solution: Downscaling Promotion Thresholds
  Simulation methodology
  Experimental Results
  Conclusions

## Slide 16: Conclusions
Conclusions
  We proved that traditional warm-up cannot be applied for HW/SW co-designed processors
    More details in the paper
  We showed that the error of the warm-up cannot be based on gCPI
  We proposed the novel warm-up approach – Downscaling Promotion Thresholds
  We proposed the model to predict the optimal warm-up setup for Downscaling Promotion Thresholds technique
    Average Simulation Error : 0.75%
    Average Simulation Cost Reduction: 65X

## Slide 17: Questions
Thanks!
?
Aleksandar Brankovic
abrankov@ac.upc.edu
?
?
?
?
?
?
?
?
?

## Slide 18: Backup Slides

## Slide 19: Compilation Plan - Issues
Compilation plan: save the plan of the region formation
Issues: cases when the region formation depends on µA execution
  Control speculation Transparent Optimization Layer (TOL): coverts biased braches into asserts
    Converting depends on how other regions are built in the code cache
  Software controlled power gating
  Software prefetcher
BB1
SuperBlock
BB2
BB3
Biased Branch?
YES
NO
Code Cache contents 1
Code Cache contents 2

## Slide 20: Results: CP (CP vs NAIVE)
Reduction in error 10-100x!!
Limitations. Depends on SW layers
NAIVE.
CP
Average error
CP.
Maximum error
20%
Average Relative Errors, collect period 10M

## Slide 21: Results: FASS vs NAIVE
NAIVE.
SW error ≠ 0
HW error ≠ 0
FEASIBLE
Maximum error
high
FASS
SW error = 0
HW error ≠ 0
NOT FEASIBLE
New technique needed!
HW
TOL
coll
HW
TOL
coll
FASS
NAIVE
0
end